## Slide 1: Portable Testing Chamber
Mueller Lab
CAD models by Jason Chen

## Slide 2: Introduction
There is a need for accessible and affordable laparoscope and camera characterization modalities
Our solution aims to be:
  Compatible option for a variety of laparoscopes and imaging test targets
  Made from accessible components that can be sourced globally
  Low-cost compared to commercial alternatives
  Easy to assemble, disassemble, and repair
    Fabricable with minimal tools
    Free of permanent fixtures (e.g., no superglue)
  Printable on a regular-sized 3D printer (220mm × 220mm footprint)

## Slide 3: Portable Testing Chamber Model
Two types of bolts used
Easy-to-print 3D-printed frame
Dovetail rails
Slide target holder
Adjustable post
Foam boards
Magnetic LED light bars for flexible positioning
Brush-lined slit
Adjustable laparoscope clamp
Rail carriers

## Slide 4: Model Close-ups

## Slide 5: Overlapping Joints
Overlapping joints create friction-fit connections and reduce external light leakage.
Boards with black outer surfaces and white inner surfaces optimize the lighting environment.

## Slide 6: Final Portable Testing Chamber Prototype
Brush opening obstructs light
Fixed to reduce material and lower costs

## Slide 7: Bench-testing Demonstration
Image test targets can be affixed here

## Slide 8: PTC Assembly Video
Protocol by Tri Quang, Ph.D., Michele Kaluzienski, Surabhi Singh, and Jason Chen
Filming and editing by Talya Simcox