## Slide 1: Auto-injector
Robert E. Fischell Institute for Biomedical Devices
Mueller Lab
CAD models by David Garvey and Jason Chen

## Slide 2: Introduction
The Auto-injector is a device that:
  Delivers three simultaneous deposits of ethyl cellulose ethanol (ECE)—a therapeutic developed by the Mueller Lab
  Relies solely on pressurized air and spring mechanisms
  Expels viscous ECE solution in a timely manner
  Retracts its needles to prevent injury
The device must also be:
  Easy to use and repair
  Compatible with a speculum
  Reusable and low-cost

## Slide 3: Auto-injector Prototype

## Slide 4: Auto-injector Prototype

## Slide 5: Exploded Assembly Animation

## Slide 6: Triple-needle Sub-assembly
Syringe tip with female Luer lock
Male Luer adapter with spin lock
1/8” ID tubing
3mm brass rod
Groove for twist-on needle cover
Adhesive applied here
Hose barb
Hose barb
Embedded threaded insert

## Slide 7: Retraction Sub-assembly and Motion
Spring-driven latch
Spring joint minimizes lateral deflection
Spring-driven latch
Alignment ribs
Alignment pins (right one hidden)
Syringe barrel is secured via a friction fit

## Slide 8: Spring-driven Retraction

## Slide 9: Pneumatic Sub-assembly
Air cylinder
Pneumatic Valve with Button
Quick disconnect external
Male Luer lock x 1/4-28 male UNF adapter
Model tubing
Aluminum syringe barrel and plunger
Air inflow from canister
ECE outflow
Quick disconnect internal
Shrader valve
ECE splitter